FRANTZ MARINE CORPORATION,INC.

139 Acadian Ln.

Mandeville, LA  70471

(985) 845-9829

M/V CHELSEA

VESSEL SPECIFICATIONS:			ENGINE SPECIFICATIONS:

TYPE			3 ½ cabin pushboat		BHP			1,000 HP

YEAR BUILT		1989				RATED		1,200 HP

BUILT BY		J & S Marine Services		MAIN ENGINES	(2) CAT 3408 TA’s

DIMENSIONS	60’ x 22’x 8’			GENERATOR	(1) 40 Kw Cummins # 4BG

TONNAGE		64 gross; 51 net					(1) 40 Kw Perkins #6.354

VISIBILITY		27’ – 360 degrees		REDUCTION		MG518 Twin disc; 6.48:1

SHAFT SIZE		5”

PROPELLER		66” X 49” SS Coolidge

WINCH		(2) 30 ton Patterson												Remote operated

CAPACITIES:					ELECTRONICS:

FUEL			20,000 gallons			STEERING		Typical full follow up

POTABLE WATER	  6,000 gallons						(2) flanking (2) rudders

LUBE OIL		     350 gallons			RADAR		(1) Furuno M-54 model R8100D

USED OIL		     300 gallons			COMMUNICATION	(1) ICOM M302 VHF radio

QUARTERS		(2) 2 man bunkrooms					(1) ICOM M59 VHF radio

1 full galley						(1) Furuno GPS

CREW										(1) Horizon LH10 loudhailer

FEATURES:	Port Main Engine CAT 3408 installed new 5/12/04

Stbd. Main Engine CAT 3408 installed 1/07/06

CAT 3408 spairs – (1) new (1) reman

(All details and specifications as reported by Owner and not guaranteed by Broker.)